## Slide 1: EDA for Mixed Signal Design
Chirayu Amin
Design and Technology Solutions
Intel Corporation
March 12, 2015
Acknowledgements Chandramouli Kashyap, Scott Little, Soner Yaldiz

## Slide 2
Timing Analysis in a Mixed Signal World
Performance Analysis in a Mixed Signal World

## Slide 3: Mixed Signal Landscape
Ingredients
PLL
CTLE
DLL
VGA
PI
DFE
Slicer
ADC
DAC
BandgapRef.
LNA
PA
Mixer
VR
Mixed Signal Design
PLL: clkout frequency = N * clkin frequency
DLL: clkout phase = clkin phase + delay
PI: clkout phase = w1*clk1in phase + w2*clk2in phase
Amplifiers: vout = A*vin
vpout-vnout = A*(vpin-vnin)
Voltage Regulator: vout = constant requested voltage
Equalizers: vout(t) = h(t)vin(t)
vout[n] = h[n]vin[n]
Slicer: vout = 1 if vin > vth, 0 otherwise
Mixer: vout freqs. = v1in freqs. ± v2in freqs.
ADC: vout[N:0] = digitized version of vina
DAC: vout = function of digital vin[N:0]
Bandgap reference: vout = constant fixed voltage

## Slide 4: Mixed Signal Landscape
Ingredients
Systems
PLL
CTLE
DLL
VGA
PI
DFE
Slicer
ADC
DAC
BandgapRef.
Sensors
Power Delivery Network
LNA
PA
Mixer
VR
DDR I/O
TX
RX
HSIO (USB)
TX
RX
Clocking Networks
Display I/O
TX
RX
RFIO
Mixed Signal Design
System Integration

## Slide 5: Mixed Signal Design Wish List
Speed and Accuracy (1 hour, 1 day)
Deal with reality
  Corners, variability, non-idealities, parameterization
  Production RTL, UVM/OVM, UPF
Startup and tuning checks
Polarity and connectivity checks
Flexibility for accuracy/speed tradeoffs
  Slow spice, fast spice, no spice
GUI instead of typing in a text editor

## Slide 6: Digital-Analog-Digital Timing
How do you characterize analog delays?
Digital FSM
Analog Circuit
clock
control code
feedback on code
b101
b100
b011
b100
time
clock
control code
feedback
What if delays depends on multiple different inputs switching in time-staggered manner?

## Slide 7: Timing for analog
PLL Feedback Divider
Frequency Divider
VCO Output Clock
Feedback Clock
Clock
Wide frequency range
What targets to use for timing analysis?

## Slide 8: Timing within analog
Decision Feedback Equalizer
Do we have a critical path?

## Slide 9: Speed and Accuracy
How to stay in “No Spice” land and still achieve “Slow Spice” accuracy?
Analog Simulator
Slow Spice Fast Spice No Spice
Digital Simulator
Accurate and Slow
Approximate and Fast
Behavioral Model
Spaceship Image Credit
Wormhole Image Credit

## Slide 10: EDA for Behavioral Modeling
Library of SV, VAMS, Verilog-A models
  Parameterizable
Parameter extraction
  From pre/post-lay netlists
Pin compatible models for drop-in spice-replacement
  N-dimensional LUTs
CTLE
DFE
CTLE 1
CTLE 2
CTLE 2
Similar to cell library characterization

## Slide 11: Stability and Optimality
Multiple control loops and tuning knobs
What algorithm to use for calibration?
  Will the design have stability problems?
  Will the tuning algorithm converge to the optimal solution for all knobs?
  What are we leaving on the table?
PLL
CTLE
DLL
VGA
PI
DFE
CDR
Slicer
Digital
FSMs

## Slide 12: Backup

## Slide 13: Using Production RTL
Do analog DEs understand RTL testbenches (OVM/UVM)?
What about unified power format?
  Analog design tools are not up to speed
What about compilation process?
  Includes
  Defines
  Arguments
  Compilation order