## Slide 1
Mixed Signal STA
Ben Farhat – Cadence Design Systems
Tau conference – March/2015

## Slide 2: Changing Landscape of MS designs
There is no longer a clear demarcation between the Digital and the Analog/Custom content of the design.
Digital content could be at various levels of hierarchy inside the analog block
  Could be hand placed standard cells or full custom cells
Very costly if timing issues are discovered late – Need for early analysis
Can’t wait till design is LVS clean to run timing analysis
Digital
Analog/
Custom
A
A
A
A
A
A
D
D
D
D
D
A
A
D
D
D
A
D
D
A
D
A
A
A
A
D
D
D
Today’s MS designs
D

## Slide 3: What are some of the options?
Spice simulation of critical paths
  Not practical if many paths
Characterization of MS blocks
  Time consuming, and need to recreate for every version
Transistor level STA -> model generation
Extend the digital timing analysis to handle Mixed Signal designs
D
A
D
A

## Slide 4: Challenges in Mixed Signal STA
Healthy inventory of legacy Mixed Signal IP’s that have not been created with connectivity in mind
Typical P&R environments can not represent many custom objects in the design
  File based interfaces between tools can not preserve custom objects in the design.
  Timing paths may contain un-characterized cells
Early timing analysis requires handling non-LVS clean data
Typical Mixed Signal designs contain many pure analog blocks
  Expose what the timer needs to see, abstract the rest
  Ability to automatically identify digital content in the design

## Slide 5: Cadence’s approach
Extend digital methodology to address MS STA challenges
Leverage full interoperability through Open Access
  Design data is shared without the need for file based translations
Ability to perform early analysis through methods similar to Interface Logic Modeling, for MS blocks
Ability to auto-detect digital paths in the design speeds the process