## Slide 1
MS Timing Challenges
Jacob Rael and Gaurav Mehta

## Slide 2: Introduction
We work in the radio group at Broadcom and deliver analog and RF IP for WLAN, Bluetooth, FM, GPS, and other radios
Our team is mostly analog and RF engineers that have no idea about digital circuitry.
Our partners are digital teams that often have no idea about analog or RF circuitry.
My modeling team works to bridge this gap

## Slide 3: Long loop to FiX STA Violations
Violation detected
Edit schematic to insert buffer
Modify layout to match schematic
Run “what if” to get buffer size
Update schematic to final buffer size
Update layout to final buffer size
Rerun STA to verify fix
D Q
D Q
D Q
D Q

## Slide 4: Dirty STA Reports
Dirty STA reports consist of the following
  Back annotation errors
  Non clocked flip flops
  Max tran and Max cap violations
Digital Teams expect clean reports so each error and violation needs to be individually fixed or waived
This process takes a long time
  Interface errors or violations not visible on radio level so need to wait until chip team runs STA
  Need find a time when everyone is available to meet. Difficult when dealing with global teams.

## Slide 5: Not much time Allocated for STA
To minimize dirty reports, timing is run close to tapeout
  Some interface clock paths are not finalized until close to tapeout
  Radio layout is evolving until tapeout date. Cleaner back annotation when the layout is finalized
With no time left to fix errors, the final timing closure occurs in a high pressure environment where marginal violations maybe waived instead of fixed properly.
  Long loop further discourages fixing violations
  “This is just a test chip.”
  “We’ll fix it next time.”

## Slide 6: Difficult to Communicate STA to Analog Designers
STA is not a simulation, it is an analysis.
  Designers feel a few analog simulations are good enough.
  Designers can reproduce these violations in simulation if given the correct corners and input sequence.
Creative use of circuit topology cells in timing critical paths breaks STA
  Add resistors to split paths or isolate nets
  Use power switches on parallel buffers to implement programmable drive strength instead of tri-state buffers
Designers don’t believe in glitch violations
  They can’t reproduce them in simulation so they don’t have any physical connection to the violation
  Maybe worst case condition can’t be put in simulation.
Analog designers are ok with layout and schematic cells having different names as long as LVS passes
  Different cell names breaks extraction and causes back annotation errors
  Difficult to fix because no one wants to change anything after the design is LVS clean

## Slide 7: Thank you